|  | High Energy High Intensity Hadron Beams |  |
| --- | --- | --- |

CARE-HHH Network: Annual Report 2005

# F. Ruggiero and W. Scandale, 20 Novembre 2005

In 2005 the networking activity of CARE-HHH was essentially focussed on the upgrade of the FAIR project at GSI and of the LHC accelerator complex at CERN.

Networking aspects: Two specific working groups were created: the first addressing issues such as accelerator physics and machine-detector interface aspects related to the upgrade of the LHC Interaction Regions, the second investigating an appropriate R&D programme for AC superconducting magnets in view of the upgrade of the LHC injector complex and of FAIR at GSI.

Deliverables: A preliminary version of the web repository for accelerator physics codes was made available in the frame of WP3 (APD). Instead the work on the database for superconducting cable and magnets in the frame of WG1 (AMT) has been further delayed owing to serious difficulties in recruiting an appropriate fellow (two potential candidates have found a better position and withdrawn their application). A Doctoral Student has been finally selected and will start working on the AMT database in January 2006.

Events: A total of 6 workshops were organized, three in the frame of WP1 (AMT), one in the frame of WP2 (ABI), and two in the frame of WP3 (APD). The ABI workshop and an additional APD mini-workshop are planned in December 2005. The participation was in general large and extended to several Institutions contributing to HHH. In two cases the participation was extended to representatives of the European Industry.

Dissemination and outreach: An intense effort was made for dissemination of information: several talks were given mostly by the HHH coordinators to illustrate the HHH activity in European laboratories and Universities or in workshops organized by other Institutions. Eleven new publications were issued and most of them are stored in the CARE database. Finally, the HHH web site was finalized and contains pages specific to each work-package and links to the HHH events and activities.

Exchanges and educational aspects: Two US accelerator specialists were hosted by CERN with the support of HHH in the frame of WP1 (AMT). Two junior scientists active in HHH issues were hosted and supported, one by CERN in the frame of WP1 (AMT), the other by the University of Sannio, Benevento, Italy in the frame of WP3 (APD). A master degree student was active at CERN on issues covered by WP1 (AMT). A master degree and a doctoral student just hired at CERN will investigate issues related to WP1 and WP3 respectively. A doctoral student has been working at CERN in 2005 on LHC IR design aspects (dipole-first).

Overall CARE-HHH Network activities in 2005 in chronological sequence

- 14/01/2005 (APD): Meeting at CERN between Accelerator Experts and representatives of ATLAS and CMS Physicists to discuss LHC Luminosity Upgrade issues, with 7 participants. http://care-hhh.web.cern.ch/care-hhh/Meetings/LHCUG20050114.txt. The discussion covered the following topics:

- Possible scenarios for the reduction of ß*,

- Possible scenarios to increase the number of bunches and discussion on the expected consequences for the experimental apparatus and on cost effectiveness aspects,

- Possible scenarios to compensate long range beam-beam, with a specific discussion on the idea of using a split-wall chamber to shield the AC long range beam-beam in the common pipe close to the LHC Interaction Points,

- Proposal of a common investigation of the interaction debris in an upgraded version of the inner triplet quadrupoles, using MonteCarlo simulation programs.

To dial with the follow up of the treated items a stable a working group and forum of discussion, called LUMIUP, with periodic meeting, was created.

  - 03/02/2005 (dissemination): A seminar summarising the outcomes of the HHH-2004 workshop was organised at CERN, in the frame of the regular AB department seminars. The talk. with the title LHC Upgraded Taking Shape - Highlights of HHH-2004: "Beam Dynamics in Future Hadron Colliders and Rapidly Cycling Synchrotrons", was jointly presented by W. Scandale and F. Zimmermann to an audience of more than 50 experts.

http://cern.ch/AB-seminar/talks/AB.Seminar.fz-HHH.pdf.

  - 17-18/02/2005 (AMT): A meeting held at CERN on the design and the prototyping of a fast-ramping superconducting pulsed dipole. The attendance was of 20 experts from CERN, INFN, GSI and CEA. The discussion covered the following items:

- Possible dipole specifications either for the construction of SIS 300 at GSI or for the upgrade of the SPS at CERN;

- Investigation on the possibility to develop a common prototyping program;

- Possible wire and cable specifications;

- Creation of a working group, named PMWG, for the follow up of the future R & D, see the web http://pmwg.web.cern.ch/PMWG/.

  - 02/03/2005 (coordination): CARE-HHH coordination meeting at CERN to review the HHH Network strategy, the sequence of future HHH events and the distribution of the P&M resources between the HHH working packages. http://care-hhh.web.cern.ch/care-hhh/Meetings/CAREHHHcoordintationmeeting02032005.txt. The main issues treated were:

- Review of alternative options,

- Review of realistic milestones and project phases,

- Discussion on possible time-table for the LHC luminosity Upgrade as requested by the CERN management;

One of the outcomes of the meeting was the identification of a few tentative milestones for future LHC machine studies, listed here:

- 2005/2006: installation and test of a beam-beam long range compensation system at RHIC to be validated with colliding beams;

- 2006/2007 new experiment for crystal collimation at the CERN-SPS;

- 2006: installation and test of Crab cavities at KEKB to validate higher beam-beam limit and higher luminosity with large crossing angles;

- 2007: if KEKB test successful, installation and test of Crab cavities in a hadron machine to validate low RF noise and emittance preservation.

  - 3-4/03/2005 (AMT): a CARE-HHH-AMT workshop was organized at CERN on Beam-Generated Heat Deposition and Quench Levels. 80 specialists from CERN, INFN, CEA, IFJ-Krakow, GSI, DESY, FNAL, University of Geneva and from SIEMENS attended it. http://amt.web.cern.ch/amt/events/workshops/beam_heat_2005/annoucement.htm. The main topics were:

- Study of the stability margin for the SC focusing triplet at the ultimate luminosity level;

- Validation of the SC quadrupole design for the LHC luminosity upgrade;

- Thermal transfer and superconducting stability;

- Thermal models and their validation through experiments;

- Comparison of codes for the simulation of thermal effects;

- Experience on quench level from LHC magnet operation and test at CERN, and from beam and magnet operation at other laboratories in the world;

  - 7-8/03/2005 (APD): CARE-HHH-APD mini-workshop ‘CC-2005’ on Crystal Collimation in Hadron Colliders held at CERN. The program and presentations are stored in the web site http://care-hhh.web.cern.ch/CARE%2DHHH/CrystalCollimation/. About 80 specialists from CERN, INFN, PNPI, IHEP, FNAL, LBNL, University of Aarhus, Helsinki Institute of Physics and University of Texas attended it. The main topics were:

- Review of the beam cleaning requirements;

- Review of crystal extraction experiments in circular accelerators;

- Experience with crystals at the various colliders;

- Crystal production, technologies and experimental procedures;

- Crystal simulation;

- Discussion on a proposal of a new experiment of crystal extraction and collimation at the CERN-SPS.

  - March-April 2005 (AMT): visit of Peter Mcintyre (University of Huston, Texas, USA) to CERN as HHH-AMT consultant for about four weeks. The main outcomes of the collaboration were:

- 18/03/2005: seminar at CERN ‘Super Dipoles for Super Colliders’, to an audience of 35 specialists; https://edms.cern.ch/cedar/plsql/doc.info?cookie=4313541&document_id=590719&version=1

- 21&30/03/2005: discussions at CERN on (i) advanced SC magnet technology and design, (ii) radiation resistant dipole to be used in dipole-first IR design; (iii) chromaticity correction for quadrupole-first IR design; (iv) LHC energy tripler using hybrid SC magnets; (v) possible counter-measures against electron cloud; (see also: http://care-hhh.web.cern.ch/care-hhh/meetings.htm);

- 04/04.2005 seminar at CERN ‘Optimizing IR design for LHC luminosity upgrade’; https://edms.cern.ch/cedar/plsql/doc.info?cookie=4313541&document_id=590724&version=1

- 14/04/2005 seminar at CERN ‘LHC Energy Tripler;

- 15/04/2005 seminar at CERN ‘Novel Method to Avoid e-cloud Limitation in the LHC’;

- 18&20/04/2005 seminars in CEA-Saclay and Dipartimento di Fisica, Milano on ‘LHC Energy Tripler’;

  - 22-23/03/2005 (AMT): CARE-HHH-AMT Topical Meeting at CERN on Insulation and Impregnation Techniques. About 30 specialists from CERN. LBLN, INFN, University of Twente, GSI, University of Texas, KEK, CEA, CIEMAT, MIT, NSCL and CCLRC, were present. http://at-hhh-amt.web.cern.ch/AT-HHH-AMT/. The main topics were:

- SC conductor insulation;

- Insulation of metallic parts;

- Insulation of inter-layers;

- Resin composition;

- Radiation resistance;

- Fibre filling and sizing;

- Heat transfer properties.

  - 30/03-02/04/2005 (dissemination): invited talk of W. Scandale at the workshop IFAE-05 in Catania (Italy) ‘LHC Status and Possible Upgrade’. The meeting was organized by the INFN and attended by about 100 physicists.

  - 05-06/04/2005 (coordination): CARE steering committee held at CERN: F. Ruggiero presented the status of CARE-HHH.

  - 06-08/04/2005 (coordination): US-LARP Collaboration Meeting in Port Jefferson, USA. Web site http://www.agsrhichome.bnl.gov/LARP/050406_danfords/. The main item of discussion was the ‘technical and resource loaded plans for FY06 and FY07’.

  - 07-08/04/2004 (dissemination): invited talk of F. Ruggiero on ‘LHC Upgrade, R&D and Impact on LHC detectors’ at the mini-workshop on Future High Energy Accelerators, CPPM, Marseille, France. Web site

http://maretude.in2p3.fr/cdsagenda/fullAgenda.php?ida=a0523.

  - April 2005 (APD): the proceedings of the workshop HHH-2004 have been completed and made available for publication as CARE and CERN Yellow Report, see: http://care-hhh.web.cern.ch/CARE-HHH/HHH-2004/Proceedings/proceedings_hhh2004.htm.

  - April 2005 (APD): a paper, written by W. Scandale and F. Zimmermann, summarising the outcome of the HHH-2004 workshop, was published in the April 2005 issue of the CERN-Courier, see http://cerncourier.com/main/article/45/3/29.

  - April 2005 (ABI): the Proceedings of the 1st CARE-N3-ABI networking meeting (held in Aumühle, 22-23/06/2004) on “Trajectory and Beam position measurements using digital techniques”, have been published (see CARE-Conf-04-024-HHH and http://adweb.desy.de/mdi/Conferencesold/Aumuehle/Proc%20CARE%20Aumuehle.pdf).  The Proceedings of the 2nd CARE-HHH-ABI networking meeting (held in Lyon, 1-2/12/2004) on “DC current transformers and beam-lifetime evaluations” has the reference CARE-Conf-04-023-HHH:  http://adweb.desy.de/mdi/CARE/Lyon/Lyon%20Proc%20final.pdf.

  - April 2005 (APD): Preliminary discussions of F. Zimmermann with M. Klein (DESY) and J. Dainton (Un. Liverpool) about "QCD-explorer": colliding ~1 TeV proton (or ion) beam from Tevatron or Super-SPS with 20-75 GeV electron beam from ILC or CLIC (first stage).

  - April 2005 (AMT): submission of the following NEST proposals:

- ‘ECOMAG’ for the Fast SC pulsed magnet for GSI and LHC injector upgrade: CERN (Scandale), GSI (Moritz), INFN (Volpini, Fabbricatore), CEA/Saclay (Rifflet);

- ‘Electron model of FFAG’, CERN (marginally) involved for LHC accelerator complex upgrade: UK(CCLRC-Lancaster-Liverpool-Oxford)-CERN-CEA/Saclay

- ‘Eurodip’, a possible extension of NED: CERN-CEA/Saclay-CIEM;

  - 13 April 2005 (APD): second meeting ‘LUMIUP’ on LHC luminosity upgrade with ATLAS and CMS physicists (8 participants). Items discussed: possible IR upgrade scenarios and implementation, identification of a team to estimate high luminosity effects of interaction debris on the superconducting triplets.

  - 19-20 May 2005 (AMT): second meeting ‘PMWG’ of the Pulsed Magnet Working Group, 19 participants, (see minutes http://pmwg.web.cern.ch/PMWG/2nd%20meeting.htm). The main goals were:

- To define an inventory of resources (tooling and personnel) who may become available.

- To review the present activity and identify possible synergies within presently available resources.

- To discuss the organization of the CARE-HHH-AMT workshop in Frascati.

  - 18-25 May 2005 (dissemination): contribution to PAC 2005 (USA):

Submitted papers related to HHH:

R. Ostojic et al. (http://care-hhh.web.cern.ch/care-hhh/Literature/MPPT043_Ostojic.pdf),

P. McIntyre et al.:

1. http://dphs10.saclay.cea.fr/Doc/Care/Files/care-conf-05-004.pdf,

2. http://dphs10.saclay.cea.fr/Doc/Care/Files/care-conf-05-006.pdf

3. http://dphs10.saclay.cea.fr/Doc/Care/Files/care-conf-05-007.pdf

  - 28/5-1/6 2005 (dissemination): invited contribution to the HIF 2005 workshop organized by the INFN. W. Scandale presented a talk ‘High Intensity Injector Chain for the LHC’ http://agenda.pi.infn.it/askArchive.php?base=agenda&categ=a0523&id=a0523s1t3/transparencies.

  - June 2005 (coordination): the two HHH coordinators became members of the “Proton Accelerators for the Future” working group newly created at CERN.

  - June 2005 (AMT): A. Devred took part to the DOE review of LARP at FNAL.

  - 8 July 2005 (APD): contribution the 61th meeting of the LHC collimation working group (see minutes http://lhc-collimation.web.cern.ch/lhc-collimation/files/minutes_2005-07-08.pdf) W. Scandale presented a possible scenario to investigate crystal collimation in the SPS in view of the LHC intensity upgrade (see transparencies http://www.cern.ch/lhc-collimation/files/WScandale 1 2005-07-08.pdf ).

  - 18-20 July 2005 (dissemination): contribution to Atlas Tracker Upgrade Workshop in Genova with more than 100 participants (see web-site: http://atu-2005.ge.infn.it/). F. Ruggiero presented the plans for the Super LHC (see transparencies

http://agenda.cern.ch/askArchive.php?base=agenda&categ=a053875&id=a053875s0t2/transparencies).

  - July 2005 (APD): publication of the proceedings of the workshop HHH-2004. http://cdsweb.cern.ch/search.py?recid=813387&ln=en.

  - July 2005 (APD): completion of the proceedings of the workshop CC-2005, http://care-hhh.web.cern.ch/CARE%2DHHH/CrystalCollimation/

  - July 2005 (APD): creation of the web page for the CARE-HHH-APD work-package. http://care-hhh.web.cern.ch/care-hhh/CARE-HHH-APD/CARE-HHH-APD.html.

  - July 2005 (APD): preliminary version of the web based code repository included in the CARE-HHH-APD work-packages.  Web site:

http://care-hhh.web.cern.ch/care-hhh/simulation_codes_catalogue_and_repository.htm

  - July 2005 (dissemination): written contribution to the HIP 05 proceeding. Author W. Scandale, title: ‘Possible scenarios for the LHC upgrade’, http://care-hhh.web.cern.ch/CARE-HHH/LUMI-05/Organization/Arcidosso/LiteratureForLumi05.html.

- 31/08-3/09/2005 (APD): CARE-HHH-APD Workshop ‘LUMI 05’on ‘Scenarios for the LHC luminosity upgrade’, Arcidosso (Italy), Web site: http://care-hhh.web.cern.ch/CARE-HHH/LUMI-05/. About 40 participants attended the meeting.

Topics:

- optical designs and luminosity performance for alternative IR layouts (dipole first vs quadrupole first (Nb-Ti or Ni3Sn) vs ironless magnet at very low ß*,

- beam-beam compensation schemes and machine-experiment interface),

- machine and magnet parameters for high energy injectors: lattice, magnet aperture, injection and extraction for new ring in the ISR tunnel, super-SPS with new transfer lines, or booster ring in the LHC tunnel.

  - 28/9-14/10 2005 (AMT): visit of H. Piekarz (Fermilab, Illinois, USA) to CERN as HHH-AMT consultant for about two weeks. The main outcomes of the collaboration were:

- proposal of the integration of a pipetron like injector in the LHC tunnel in collaboration with G. De Rijk (CERN);

- 10/10/2005: seminar at CERN on ‘Pipetron Technology’;

- 13/10/2005: discussions at CERN on the possibility to use a pipetron-like injector for LHC, to be installed in the LHC tunnel providing protons of up to 1.5 TeV/c momentum.

- 28/9–01/10 2005 (dissemination): contribution to the 8th ICFA Seminar on ‘Future Perspectives in High Energy Physics’, Kyungpook National University, Daegu, Korea, with about 170 participants. F. Ruggiero presented the plans for the LHC Luminosity Upgrade (see transparencies at http://chep.knu.ac.kr/ICFA-Seminar/upload/9.29/Morning/session1/Ruggiero-ICFA-05.pdf)

- 3-4 October 2005 (APD): US-LARP mini-Workshop on ‘LHC IR upgrade’, FNAL, attended by 3 CERN scientists associated to CARE. Web site: http://larp.fnal.gov/IR2005/

topics:

- heat deposition and magnet quench limits,

- TAS/TAN integration and follow-up of HHH-2004 workshop,

- feasibility of large crossing angles and CRAB cavities in hadron storage rings,

- beam-beam compensation schemes.

- 5-6 October 2005 (coordination): US-LARP coordination meeting, FNAL, attended by F. Ruggiero. About 35 participants.

- 24 October 2005 (coordination): HHH coordination meeting at CERN in view of CARE05

- 26-28 October 2005 (AMT): CARE-HHH-AMT Workshop ‘ECOMAG05’ on SC Pulsed Magnets for Accelerators, Frascati, 70 particitants from CERN, INFN ENEA, GSI, CEA, EPFL, JINR, MIT, CIEMAT, KEK, IHEP, EFDA, Bochvan institute of Inorganic Materials, University of Twente, Ohio State University and from 6 European  Industries acting on SC magnets or SC materials (Alstom, Accell, NBB, Bruker BioSpin, Ouctokumpu, Ansaldo). Web site http://ecomag-05.web.cern.ch/ecomag-05/.

Topics:

- define a set of agreed parameters for the development of SC magnets ranging from low field, continuously pulsed (typically 2 T peak, 4 T/s, 100 mm aperture, 108 cycles) to medium field, high-duty cycle magnets for storage and booster rings (typically 6 T peak, 1 T/s, 80 mm aperture, 106 cycles),

- translate the requirements into specifications for performance of strand, cable, magnet and auxiliaries,

- define the R&D required to achieve the above specifications and produce a tentative road-map for rement and prototyping activity.

- 10 November 2005 (APD): LHC Seminar given at CERN by F. Ruggiero and W. Scandale on “Scenarios for the LHC Luminosity Upgrade”, in the presence of some 120 scientists. http://agenda.cern.ch/fullAgenda.php?ida=a057227.

- F. Ruggiero http://care-hhh.web.cern.ch/care-hhh/Seminars/Ruggiero-LHC-Seminar-10-11-05.pdf.

- W. Scandale http://care-hhh.web.cern.ch/care-hhh/Seminars/Scandale-LHC-Seminar-10-11-05.pdf.

- 11 November 2005 (AMT): Debriefing of the outcome of the workshop ECOMAG05, aiming at:

  - synthesis of the discussions of the ECOMAG05

  - identification of a possible roadmap for the R&D on AC superconducting magnets at CERN and GSI

  - proposal for common developments and technical solutions

  - 30 participants

- 6-7 December 2005 (ABI): CARE-HHH-ABI Workshop on “Remote diagnostics and maintenance of beam instrumentation devices”, Hirschberg (close to Heidelberg, Germany), attended by about 20 invited contributors associated to CARE.  http://adweb.desy.de/mdi/CARE/Hirschberg/ABI-Hirschberg.htm

Topics:

- review the objectives and the outcome of previous initiatives on remote accelerator operation or accelerator diagnostics

- define realistic objectives for the operation and diagnostics of future hadron accelerators (including LHC@FNAL)

- discuss in detail technology issues related to this subject

propose concrete HHH-ABI workpackages and milestones for the coming 18 months in order to meet the specified objectives.

| HHH Activity 2005 | January | February | March | April | May | June | July | August | September | October | November | December |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Activity yearly and/ or steering meeting |  |  | 2 CERN (CH) coordination meeting | 5&6 CERN (CH) steering meeting |  |  |  |  |  |  |  |  |
| Meeting/Workshop WP1 AMT |  |  | 3-4 workshop CERN (CH); 22-23 workshop CERN (CH) |  |  |  |  |  |  | 26-28 ENEA (I) ECOMAG05 workshop | 11 CERN (CH) ECOMAG05 debriefing |  |
| Meeting/Workshop WP2 ABI |  | 3 CERN (CH) AB seminar |  |  |  |  |  |  |  |  |  | 6-7 workshop Hirschberg (DE) |
| Meeting/Workshop WP3 APD |  |  | 7-8 workshop CC-2005 CERN (CH) |  |  |  | 8 collimation WG CERN (CH) |  | 31/08-03/09 LUMI05 (Arcidosso I) workshop |  | 10 CERN LHC seminar |  |
| Workshop with other CARE activities |  |  |  |  |  |  |  |  |  |  |  |  |
| Working groups |  |  |  |  |  |  |  |  |  |  |  |  |
| PMWG |  | 17-18 CERN (CH) |  |  | 19-20 CERN (CH) |  |  |  |  |  |  |  |
| LUMIUP | 14 CERN (CH) |  |  | 13 CERN (CH) |  |  |  |  |  |  |  |  |
| Conferences & workshops |  |  |  |  |  |  |  |  |  |  |  |  |
| PAC05 |  |  |  |  | 18-25 four contributed papers |  |  |  |  |  |  |  |
| US-LARP |  |  |  | 6-8 P. Jefferson collaboration meeting |  |  |  |  |  | 3-4 workshop; 5-6 collaborat. meeting, FNAL |  |  |
| HIF2005 |  |  |  |  | 29 invited talk |  | 29 written contribution |  |  |  |  |  |
| IFAE2005 |  |  | 30/03-02/04 invited talk |  |  |  |  |  |  |  |  |  |
| CPPM Marseille |  |  |  | 7-8 invited talk |  |  |  |  |  |  |  |  |
| ATU2005 |  |  |  |  |  |  | 18 invited talk |  |  |  |  |  |

Table 1: Overview of meetings, workshops and events (co-)organized by the HHH Network or with HHH contributions in 2005

Table 2: List of meetings, workshops and events (co-)organized by the HHH Network or with HHH contributions during 2005

| Date | Title/subject | location | Main organizer | Number of participants | Comments and Web site |
| --- | --- | --- | --- | --- | --- |
| 14 Jan | 1st LUMIUP meeting | CERN (CH) | HHH-coordinators | 7 | Discussion on LHC luminosity upgrade scenarios. http://care-hhh.web.cern.ch/care-hhh/Meetings/LHCUG20050114.txt |
| 3 Feb | AB seminar | CERN (CH) | AB-seminar-coordinator | About 50 | LHC Upgraded Taking Shape – Highlights of HHH-2004: “Beam Dynamics in Future Hadron Colliders and Rapidly Cycling Synchrotrons” W. Scandale (part I), F. Zimmermann (part II) http://cern.ch/AB-seminar/talks/AB.Seminar.fz-HHH.pdf. |
| 17-18 Feb | 1st PMWG meeting | CERN (CH) | HHH-coordinators | About 20 | Pulsed Magnet Working Group meeting. http://pmwg.web.cern.ch/PMWG/1st%20meeting.htm |
| 2 Mar | CARE-HHH coordination meeting | CERN (CH) | HHH-coordinators | 5 | Review of the HHH activity http://care-hhh.web.cern.ch/care-hhh/Meetings/CAREHHHcoordintationmeeting02032005.txt |
| 3-4 Mar | 2 nd HHH-AMT workshop | CERN (CH) | HHH-AMT (WP1) coordinators | 80 | Review of beam-generated heat deposition and quench levels in SC magnets. http://amt.web.cern.ch/amt/events/workshops/beam_heat_2005/annoucement.htm. |
| 7-8 Mar | 2 nd HHH-APD mini-workshop | CERN | HHH & HHH-APD (WP3) coordinators | About 80 | Review of crystal assisted extraction and collimation in circular accelerators. http://care-hhh.web.cern.ch/CARE%2DHHH/CrystalCollimation/ |
| Mar & Apr | Meeting with and seminars by P. Mcintyre | CERN (CH) | HHH-coordinators | From 20 to 80 | http://care-hhh.web.cern.ch/care-hhh/meetings.htm |
| 22-23 Mar | 3 rd HHH-AMT workshop | CERN (CH) | R. Maccaferri (CERN) & S. Gourlay (NLBL) | 32 | Review of insulation in SC magnets. http://at-hhh-amt.web.cern.ch/AT-HHH-AMT/. |
| 30 Mar – 2 Apr | IFAE 2005 | Catania (I) | Ad hoc committee of INFN Catania | About 100 | Review High Intensity physics experiments. http://cms.ct.infn.it/ifae/ |
| 5-6 Apr | CARE steering committe | CERN (CH) | CARE-coordinators | About 20 | http://care.lal.in2p3.fr/CAREmeetings/Management/Steering/april-05-05/HHH.ppt |
| 6-8 Apr | US-LARP collaboration meeting | Port Jefferson (USA) | US-LARP-coordinators | About 60 | Financial issues for FI2006 and FY 2007 http://www.agsrhichome.bnl.gov/LARP/050406_danfords/ |
| 7-8 Apr | Mini-workshop on Future Hadron Acc. | Marseille (F) | Ad hoc organizing committee | About 30 | Issues related to future hadron colliders; http://maretude.in2p3.fr/cdsagenda/fullAgenda.php?ida=a0523 |
| 13 Apr | 2nd LUMIUP meeting | CERN (CH) | HHH-coordinators | 8 | Discussion on LHC luminosity upgrade scenarios. Web summary not yet available |
| 18-25 May | PAC 2005 | USA | PAC committee | 700 | http://care-hhh.web.cern.ch/care-hhh/Literature/MPPT043_Ostojic.pdf http://dphs10.saclay.cea.fr/Doc/Care/Files/care-conf-05-004.pdf http://dphs10.saclay.cea.fr/Doc/Care/Files/care-conf-05-006.pdf http://dphs10.saclay.cea.fr/Doc/Care/Files/care-conf-05-007.pdf |
| 19-20 May | 2nd PMWG meeting | CERN (CH) | HHH-coordinators | 19 | Pulsed Magnet Working Group meeting. http://pmwg.web.cern.ch/PMWG/2nd%20meeting.htm |
| 29 May | HIF 2005 | Elba Island (I) | INFN | 80 | http://agenda.pi.infn.it/askArchive.php?base=agenda&categ=a0523&id=a0523s1t3/transparencies |
| 8 July | 61th Collimation Working Goup | CERN (CH) | CERN Collimation Team | 15 | http://lhc-collimation.web.cern.ch/lhc-collimation/files/minutes_2005-07-08.pdf http://www.cern.ch/lhc-collimation/files/WScandale 1 2005-07-08.pdf |
| 18-20 July | ATU2005 | Genova (I) | INFN | 100 | http://atu-2005.ge.infn.it/ http://agenda.cern.ch/askArchive.php?base=agenda&categ=a053875&id=a053875s0t2/transparencies |
| 29 Jul | HIP 2005 | Elba Island (I) | INFN | 80 | http://care-hhh.web.cern.ch/CARE-HHH/LUMI-05/Organization/Arcidosso/LiteratureForLumi05.html |
| 31 Jul-3 Sep | LUMI 05 | Arcidosso (I) | HHH & HHH-APD (WP3) coordinators | 40 | Scenarios for the LHC Luminosity Upgrade. http://care-hhh.web.cern.ch/CARE-HHH/LUMI-05/ |
| 28 Sep- 1 Oct | ICFA Seminar | Daegu (Korea) | ICFA | 170 | Future Perspectives in High Energy Physics http://chep.knu.ac.kr/ICFA-Seminar/ |
| 3-4 Oct | US-LARP mini-workshop | FNAL (USA) | LARP coordinators | 50 | http://larp.fnal.gov/IR2005/ |
| 5-6 Oct | US-LARP collab. meeting | FNAL (USA) | LARP coordinators | 35 | http://larp.fnal.gov/Oct05Collaboration/ |
| 24 Oct | HHH coordinat. meeting | CERN (CH) | HHH-coordinators | 4 | Minutes sent out by email to CARE-HHH WP coordinators and deputies |
| 26-28 Oct | ECOMAG 05 | Frascati (I) | HHH & HHH-AMT (WP1) coordinators | 70 | http://ecomag-05.web.cern.ch/ecomag-05/ |
| 10 Nov | LHC seminar | CERN (CH) | LHC-seminar-coordinator | 120 | http://agenda.cern.ch/fullAgenda.php?ida=a057227 |
| 11 Nov | AT seminar | CERN (CH) | W. Scandale | 30 | Web site not yet available |
| 6-7 Dec | HHH-ABI workshop | Hirschberg (DE) | HHH-ABI coordinators | About 20 | Remote diagnostics and maintenance of beam instrumentation devices. http://adweb.desy.de/mdi/CARE/Hirschberg/ABI-Hirschberg.htm |

Table 3: List of talks to workshops and conferences made by HHH members and which are about (or include) activities carried within HHH

| # | Subject | Speaker/Lab | Event | Date | Talk Web site | CARE-Conf |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | LHC Upgrade | W.Scandale & F. Zimmermann /CERN | AB seminar | 03/02/2005 |  |  |
| 2 | Collider Technologies | P. Mcinthyre /CARE expert | AT seminar | 18/03/2005 |  |  |
| 3 | Magnet Technologies | P. Mcinthyre /CARE expert | AT seminar | 04/04/2005 |  |  |
| 4 | LHC Energy Tripler | P. Mcinthyre /CARE expert | AT seminar | 14/04/2005 |  |  |
| 5 | Cure for e-cloud | P. Mcinthyre /CARE expert | AT seminar | 15/04/2005 |  |  |
| 6 | LHC Energy Tripler | P. Mcinthyre /CARE expert | Seminar in Dip. di Fisica di Milano | 18/04/2005 |  |  |
| 7 | LHC Energy Tripler | P. Mcinthyre /CARE expert | CEA/Saclay seminar | 20/04/2005 |  |  |
| 8 | LHC Upgrade | W. Scandale /CERN | IFAE 2005 | 31/03/3005 | http://agenda.cern.ch/askArchive.php?base=agenda&categ=a051438&id=a051438s6t1/moreinfo |  |
| 9 | HHH status report | F. Ruggiero /CERN | CARE-steering committee | 06/04/2005 | http://care.lal.in2p3.fr/CAREmeetings/Management/Steering/april-05-05/HHH.ppt |  |
| 10 | LHC Upgrade | F. Ruggiero /CERN | CPMP meeting /Marseille | 07/04/2005 | http://atu-2005.ge.infn.it/ |  |
| 11 | LHC Injector Upgrade | W. Scandale /CERN | HIF 2005 | 29/05/2005 | http://agenda.pi.infn.it/askArchive.php?base=agenda&categ=a0523&id=a0523s1t3/transparencies |  |
| 12 | Crystal Collimation | W. Scandale /CERN | 61th Collimation WG | 08/07/2005 | http://www.cern.ch/lhc-collimation/files/WScandale 1 2005-07-08.pdf |  |
| 13 | LHC Upgrade | F. Ruggiero /CERN | ATU 2005 | 18/07/2005 | http://agenda.cern.ch/askArchive.php?base=agenda&categ=a053875&id=a053875s0t2/transparencies |  |
| 14 | LHCI injector I | H. Piekarz /FNAL | AT seminar | 10/10/2005 |  |  |
| 15 | LHCI injector II | H. Piekarz /FNAL | AT seminar | 13/10/2005 |  |  |
| 16 | LHC upgrade | F. Ruggiero /CERN | LHC seminar | 10/11/2005 | http://care-hhh.web.cern.ch/care%2Dhhh/Seminars/Ruggiero-LHC-Seminar-10-11-05.pdf |  |
| 17 | LHC injectors | W. Scandale /CERN | LHC seminar | 11/11/2005 | http://care-hhh.web.cern.ch/care%2Dhhh/Seminars/Scandale-LHC-Seminar-10-11-05.pdf |  |

# Table 4: List of document issued by HHH-participants

| # | CARE document type and number | Title | Authors and Labs | Date |
| --- | --- | --- | --- | --- |
| 1 | CARE-Conf-04-24-HHH | Proceedings of the 1st CARE-N3-ABI networking meeting |  | April 2005 |
| 2 | CARE-Conf-04-23-HHH | Proceedings of the 2nd CARE-N3-ABI networking meeting |  | April 2005 |
| 3 | CARE-Conf-05-01-HHH | Proceedings of the ECLOUD'04 Workshop | Editor F. Zimmermann |  |
| 4 | CARE-Conf-05-02-HHH | Proceedings of the HHH 2004 Workshop | Editor F. Zimmermann |  |
| 5 | CARE-Conf-05-04-HHH | On the feasibility of a tripler upgrade for LHC | P. McIntyre, A. Sattarov | May 2005 |
| 6 | CARE-Conf-05-05-HHH | Low-ß quadrupole design for the LHC luminosity upgrade | R. Ostoijc et al. | May 2005 |
| 7 | CARE-Conf-05-06-HHH | Towards an optimization of the LHC intersection region using new magnet technology | P. McIntyre, A. Sattarov, J.P. Koutchouk | May 2005 |
| 8 | CARE-Conf-05-07-HHH | Killing the electron cloud effect in the LHC arcs | P. McIntyre, A. Sattarov | May 2005 |
| 9 | CARE-Conf-05-21-HHH | Electron cluod measurements in the SPS in 2004 | G. Arduini, V. Baglin, J.M. Jimenez, F. Ruggiero. D. Schulte, F. Zimmermann | May 2005 |
| 10 | CARE-Report-05-08-HHH | Annual report on the HHH collaboration | F. Ruggiero, W. Scandale | Jan 2005 |
| 11 | CARE-Report-05-15-HHH | First 2005 intermediate report on the HHH collaboration | F. Ruggiero, W. Scandale | April 2005 |
| 12 | CARE-Report-05-22-HHH | Second 2005 intermediate report on the HHH collaboration | F. Ruggiero, W. Scandale | Sep 2005 |

Table 5: Temporary staff hiring

| # | Lab | Job Type | Duration | Work subject | Status |
| --- | --- | --- | --- | --- | --- |

Table 6: Status of the lowest Sub tasks level in the WP which are supposed to have started according to the MS project breakdown in Annex 1

| WBS # | Title | Original begin date (Annex 1) | Original end date (annex1) | Estimated Status | Revised end date |
| --- | --- | --- | --- | --- | --- |
| General | MS: annual HHH meeting |  |  |  |  |
|  | HHH coordination meeting (ID8) | T1-2005 | T2-2005 | 100 % |  |
| WP1-AMT | MS: AMT topical meeting on Insulation and Impregnation Techniques | T1-2005 | T1-2005 | 100 % | On time: T1-2005 |
|  | MS: AMT workshop on Beam Generated heat and Magnet Quench Level | T1-2005 | T1-2005 | 100 % | On time: T1-2005 |
|  | Web-based database for SC cable and magnets | T3-2004 | T4-2006 | 10 % | Delayed to T4-2007 |
|  | MS: specific meeting on database | T2-2005 | T2-2005 | 0 % | Delayed to T4-2005 |
|  | ID: first report on web based database | T2-2005 | T2-2005 | 0 % | Delayed to T4-2005 |
|  | Catalogue of numerical codes for AMT1 and AMT4 | T1-2004 | T4-2005 | 20 % | Delayed to T4-2006? |
|  | Comparison of codes for AMT1 and AMT4 | T1-2004 | T2-2004 | 20 % | Delayed to T4-2005 |
|  | Identifications of main limiting issues | T2-2004 | T4-2004 | 20 % | Delayed to T2-2005 |
|  | ID: Proceedings of the first topical workshop on superconductors | T1-2005 | T1-2005 | 100 % | On time: T1-2005 |
|  | ID: report on AMT organization and conductor development | T1-2005 | T1-2005 | 80 % | Delayed to T3-2005 |
|  | Comparative studies of alternatives using low field magnets for AMT2 and AMT3 | T3-2004 | T4-2004 | 30 % | Delayed to T3-2005 |
|  | Identification of general issues relevant for magnet design for AMT5 | T3-2004 | T4-2004 | 10 % | Delayed to T4-2005 |
|  | Review of the development in US and for ITER on conductors and magnet technology relevant for AMT1 and AMT2 | T1-2005 | T1-2005 | 90 % | Delayed: T3-2005 |
|  | Comparative studies for alternatives using low field magnets for AMT2 and AMT3 | T4-2004 | T2-2005 | 20 % | Delayed to T4-2005 |
|  | Determination of scaling law for magnets and cryogenic cost for AMT5 | T4-2004 | T2-2005 | 20 % | Delayed to T3-2005 |
|  | MS: preliminary report on scaling law for magnets and cryogenic cost for AMT5 | T2-2006 | T2-2006 | 20% | Delayed to T4-2006 |
| WP2-ABI | ID: proceedings of the first ABI topical workshop | T1-2005 | T1-2006 | 100 % | On time: T1-2005 |
|  | ID: proceedings of the second ABI workshop | T2-2005 | T3-2005 | 90 % | On time: T2-2005 |
| WP3-APD | Comparison of alternative synchrotron and IR design | T1-2004 | T2-2004 | 75 % | Delayed to T3-2005 |
|  | ID: proceedings of the first APD workshop | T1-2005 | T1-2005 | 100 % | On time: T1-2005 |
|  | Second topical workshop | T1-2005 | T1-2005 | 100 % | On time: T1-2005 |
|  | MS: general APD meeting | T2-2005 | T2-2005 | 0 % |  |
|  | ID: First structured list of intensity limits for booster synchrotrons and LHC | T2-2006 | T2-2006 | 50% | Delayed: T3-2006 |

# Table 7: Status with respect to the interim reports and deliverables to be done in 2005 according to the MS project breakdown

| WBS # | Title | Due date in Annex 1 | Status | Revised delivery date |
| --- | --- | --- | --- | --- |
| General | - | - | - |  |
| WP1-AMT |  |  |  |  |
| 15 | MS: AMT topical meeting on Insulation | T1-2005 | 100 % | T1-2005 |
| 16 | ID: proceedings if the first AMT topical workshop on superconductors | T1-2005 | 100 % | T1-2005 |
| 17 | ID: report on AMT organization and conductor development | T4-2004 | 80 % | T2-2005 |
| 19 | MS: AMT topical meeting on Beam loss induced thermal effects | T1-2005 | 100 % | T1-2005 |
| WP2-ABI |  |  |  |  |
| W3-APD |  |  |  |  |
| 48 | MS: proceedings of the first topical APD workshop | T1-2005 | 100 % | T1-2005 |
| 49 | ID: meeting on simulation code bench marks | T1-2005 | 0 % | T3-2005 |

NOTE: The development of the web-based database for SC cables and magnets has been slowed down. The main reasons of the delay are that the budget to hire a dedicated fellow was not yet available in T2-2005; later on, it turned out to be non-trivial to recruit an adequate candidate.

Table 8: Status of the expenditures per participant and activity (in €)

| participants | Integrated cost for permanent staff in 2004 | Integrated cost for permanent staff in 2004 | Integrated cost for equipment in 2004 | Integrated cost for consumable in 2004 | Integrated cost for travel in 2004 |
| --- | --- | --- | --- | --- | --- |
|  | engaged | spent | engaged | spent | engaged | spent | engaged | spent | engaged | spent |
| 01. CEA |  |  |  |  |  |  |  |  |  |  |
| 04. GSI |  |  |  |  |  |  |  |  |  |  |
| 05. DESY |  |  |  |  |  |  |  |  |  |  |
| 10. INFN |  |  |  |  |  |  |  |  |  |  |
| 11. TEU |  |  |  |  |  |  |  |  |  |  |
| 15. WUT |  |  |  |  |  |  |  |  |  |  |
| 16. CSIC |  |  |  |  |  |  |  |  |  |  |
| 17. CERN |  |  |  |  |  |  |  |  |  |  |
| 19. PSI |  |  |  |  |  |  |  |  |  |  |
| 20. CCLRC |  |  |  |  |  |  |  |  |  |  |

Table 9 Gantt table of the HHH Network progress in 2005

Table 10 Gantt table of the HHH Network progress expected in the next 18 months